## Slide 1: Super widefield particle tracking in near real-time via image stitching
Sean MacKenzie, Rami Dabit, Pete Li
ECE 278A

## Slide 2: Introduction
A classic problem in microscopy
resolution range
For example, for 20X magnification:
Field-of-view (FoV; i.e. range) is ~250 um2.
spatial (x, y, z) resolution is ~ FoV / 100.
Wants: FoV ~1 mm2
Needs: ~ 1 m
Limitations: ~ FoV -1
Application: Microfluidic Particle Tracking
Presenter: Sean
Notes: Currently, this requires performing multiple experiments where each local region-of-interest is separately observed.
This has a significant drawback:
  experimental conditions can vary unpredictably and uncontrollable, lowering experiment repeatability and confidence.

## Slide 3: Super widefield imaging via image stitching
Step 1. Image Acquisition
ImageN (x, y, z, time)
Step 2. Image-to-image stitching
Imagei (xi, yi, zi, ti)  Imagei+1 (xi + x, yi + y, zi + z, ti + t)
Step 3. Super widefield image reconstruction
Image =
Imagei
Imagei+1
Imagei+2
Presenter: Sean

## Slide 4: Methods – Image Stitching
Feature Detection
  Laplacian of Gaussian (LoG)
  Difference of Gaussian (DoG)
  Determinant of Hessian (DoH)
Keypoint Preselection
  Manually define # of key points
  RANSAC
  Least Median of Squares (LMS)
Keypoint Matching
  Custom implementation: SSD minimization
  SIFT
  Nonlinear least squares
Stitching
Post-processing Bundle Adjustment
Presenter: Rami

## Slide 5: Methods – Dataset
Synthetic particle images
  Access to ground truth.
  Standardized dataset.1
  Widely used.2
50%
25%
Investigate: Percent image ovlerap
% overlap
Dataset #1
Dataset #2
i
j
Widefield image for 2D stitching
Image for 1D stitching
[1] M. Rossi, (2020)
[2] Pennathur Lab, Dept. of Mechanical Enginerring, UCSB
Presenter: Sean

## Slide 6: 2. Keypoint Selection
(1) Manually define # of key points
Manually define # of key points
RANSAC
Least Median of Squares (LMS)
key points = 14
matching points:
un-matched points:
Imagei
Imagei+1
25 m
Presenter: Rami and Peter
Note to Peter and Rami:
You may want to add more info here

## Slide 7: 3. Keypoint Matching – SSD Minimization
Routine:
  For key point1 in imagei (img0)
    Find the nearest key point in imagei+1 (img1)
    Calculate the pixel-wise “distance”:
      Evaluate the Gaussian-weighted sum of squared difference over a pixel neighborhood (e.g. 11x11 pixels)
    Return the pixel with the smallest distance.
  Repeat for all key points1…N
  imagei
  (img0)
  imagei+1
  (img1)
Presenter: Peter

## Slide 8: 3. Keypoint Matching – SSD Minimization
  imagei
  (img0)
  imagei+1
  (img1)
Presenter: Peter
radius
2*radius + 1
point-wise product
point1 at img0
point1 at img1
Gaussian-weighted matrix
-
x
(
)
center
1st step: compute diff matrix
2nd step: compute sum of elements in diff matrix
(radius=2 at the example)

## Slide 9: Algorithm Mechanism
Use matching points
to stitch images.
Use detector to extract positions of the particles.
Update the # of key points
Obtain matching points by SSD minimization
Update input images
Start
Presenter: Peter

## Slide 10: Results – Number of Key Points
Reference Image
Matching Image
ImageN
Continuous image stitching
X
Identified key point
X
SSD 0
50%
image overlap
25%
image overlap
Presenter: Sean

## Slide 11: Results – Percent Image Overlap
1. Identified two “best” stitching implementations.
50%
image overlap
25%
image overlap
stitching error,
2. Evaluated super widefield 2D stitching accuracy for 25% and 50% image overlap.
Presenter: Sean

## Slide 12: Conclusion
Key Takeaways:
Evaluating pointwise matching accuracy is not necessarily indicative of image stitching accuracy.
   Example: 25% overlap with DoH with 10 key points had lower matching accuracy but perfect stitching accuracy.
Increasing the # of key points generally increases accuracy.
  Example: 25% overlap with DoH with 10 key points.
Increasing the image overlap generally increases the accuracy.
  But perfect stitching was demonstrated at 25% overlap.
  Enables faster scanning of super widefield area.
Presenter: Sean

## Slide 13: Thank you! Questions?

## Slide 15: Supplementary Information

## Slide 16: Outline
Introduction + Background
  microscopes are limited by field-of-view
Solution
  stitching images together to capture a widefield
Methods
  Feature Detection
    Difference of Gaussian (DoG), Determinant of Hessian (DoH), Corner Harris
  Keypoint Preselection
    Manual Input
  Matching
    Custom Gaussian Weighted SSD
  Stitching
  Post-processing Bundle Adjustment
Results and Discussion
  Number of Key Points
  Percent Image Overlap
Conclusion

## Slide 17: 1. Feature Detection
Difference of Gaussians (DoG)
Determinant of Hessian (DoH)
Harris Corner Detector

## Slide 18: Future Directions
Vertical
Horizontal
Arbitrary 2D
Arbitrary 3D
Present Work
Future Work

## Slide 19: Evaluation Metrics
Metric | Variable Name | Description
Ground Truth | true_image_length | The ground truth image length.
 | true_image_width | The ground truth image width.
 | true_percent_overlap | The percent overlap of the synthetically generated images.
 | true_shift | The pixel shift described by the true percent overlap.
Inputs | input_direction | The direction of the image stitching (e.g., horizontal or vertical)
 | input_detector | The key point detector (e.g., Difference of Gaussians)
 | input_num_keypoints | The number of key points used for image stitching.
 | input_min_distance | The minimum distance (in pixels) allowable for some key point detectors.
Outputs | image_number | The image number along a stitching path where 0 is the first image.
 | num_keypoints_detected | The number of key points detected in the image.
 | num_keypoints_matching | The number of key points used for image stitchings (dependent on detection).
 | sum_ssd | The sum of the sum squared difference over all matching points between two images.
 | calc_shift | The calculated shift to stitch two images together.
 | calc_diff | A quantitative metric of the image stitching error (note: not used for evaluation).
 | calc_image_length | The reconstructed image length.
 | calc_image_width | The reconstructed image width.